## Slide 2: Telecommunicatiesystemen
Mobile IP
Johan Bergs – Jeremy Van den Eynde

## Slide 3: Motivation for Mobile IP
IP Routing
  based on IP destination address, network prefix (e.g. 143.129.70) determines physical destination subnet
  Problem in case of mobility: change of physical subnet implies inconsistency between IP address and actual location
  Potential solutions: specific routes or change of IP address
Specific routes to end-systems?
  change of all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile node, DNS (translation logical name  IP address) updates take to long time
  TCP connections break

## Slide 4: Requirements to Mobile IP (RFC 5944, before: RFC 3344)
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  transparent for higher layer protocols and applications
Compatibility
  support of the same layer 2 protocols as standard IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems
Security
  authentication of all registration messages
Efficiency and scalability
  only little additional messages to the mobile system required
  support of a large number of mobile systems in the whole Internet

## Slide 5: Entities involved in Mobile IP
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the Care-of-Address (CoA)
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
  forwards the tunneled datagrams to the MN, typically also the default router for the MN

## Slide 6: Entities involved in Mobile IP
Care-of Address (CoA)
  IP address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  Two possibilities:
    Foreign Agent CoA: the CoA is an IP address of the FA; the FA has to forward the packet to the MN
    Co-located CoA: The MN acquires temporarily an additional IP address which is topologically correct. In view of the address space, this CoA is used in IPv6
Correspondent Node (CN)
  communication partner

## Slide 7: Entities involved in Mobile IP
mobile end-system
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN
Internet

## Slide 8: Data transfer to the mobile system
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN
Internet

## Slide 9: Data transfer from the mobile system
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN
Internet

## Slide 10: Mobile IP: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 11: Network integration (1)
Agent discovery
  Two methods: Agent Advertisement and Agent Solicitation
  Agent Advertisement
    HA and FA periodically send advertisement messages into their physical subnets (router advertisement ICMP messages RFC 1256)
    MN listens to these messages and detects, if it is in the home or a foreign network (standard case for home network)
    MN reads a Care-of-Address (COA) from the FA advertisement messages
  Agent Solicitation
    MN generates Agent Solicitation when it does not want to wait for agent advertisement
    Agent solicitation is based on router solicitation (RFC 1256)

## Slide 12: Network Integration (2)
Registration (always limited lifetime!)
  MN signals COA to the HA via the FA (if FA CoA is used)
  HA acknowledges via FA to MN (or directly if co-located CoA is used)
  This registration is only valid for a limited time and needs to be renewed regularly (soft-state)
  these actions have to be (or better, should be) secured by authentication
  Upon receiving a registration request, the HA sets up a mobility binding
    This is a binding between MN’s home IP address and its current CoA
    This binding contains a lifetime
Advertisement
  HA advertises the IP address of the MN (as for fixed systems), i.e. standard routing information
  routers adjust their entries, these are stable for a longer time (HA responsible for a MN over a longer period of time)
  packets to the MN are sent to the HA, independent of changes in COA/FA